Pre Drive Check List

Approach vehicle assessing it as you do so for general condition.

Look at parking brake, physically check it is applied & that it is out of gear.

Proceed around the vehicle still checking general condition,   pay special attention to the all doors & windows, wheel arches, spray suppression equipment, tyres (tread depth 1mm across 75% of the width & all the way round, no cuts or bulges), wheels, nuts, reflectors fitted & potential places that persons could hide especially the underside.

On the rear check lights for damage, number plate.

Is the load within the vehicles official payload? - i.e. Not overloaded.

Is the load correctly loaded & secured?

Fasten doors, check for other doors.

Do your mirrors allow you an effective view down the sides of the vehicle to the legal spec (see mirror doc)?