Brake away cables

There has been a lot of discussion recently on FB groups re the right way to clip the brake away cable. Many pointing to the old Alko document from circa 2003 showing looping just the ball.

That advice has been superseded.

Since 2013 the EU regs were updated to include regulation 55. This regulation made it necessary for towbar makers to fit & test a proper brake away cable connection point. If fitted this point should be used or at least a point as secure IE through the bar. Looping the ball should ONLY ever be seen as a last ditch attempt that is JUST better than nothing.

There has also been much said re the two clip types.

The older spring metal ones & newer carabineer type.

Alko do recommend that the older type is looped around an item (but not just the ball neck) & then clipped back to the cable.

The newer type can be direct clipped or looped.

That is the official makers advice & should be followed.

Once the cable is fitted ensure that with the brake released it is not going to drag on the floor or snag in a turn.

These are all suitable methods

These are last ditch only if no other method is available

It is easy to see how they could jump off with the hitch in a separation.

You can buy cable connection points to add to your car if it does not have a fitted one.