Hitching & Unhitching

Uncoupling 1 to 6

Park on flat level ground were possible

Tow vehicle handbrake on, select neutral & turn engine off KEY OUT

1, Apply trailer brake or chock wheels if no brake fitted

2, Uncouple electrics, stow plug/s

3, STANDARD JOCKEY WHEEL

Lower jockey wheel to aprox 3” from the ground and lock in place, wind down jockey wheel to touch the ground

3, NEW STYLE JOCKEY WHEEL

Wind down jockey wheel to touch the ground ensuring the wheel locks in place.

4, Lift coupling release (press button etc) & tilt forward, wind down jockey wheel to raise coupling clear of the towing ball by aprox 2”

5, Check trailer brake is effective, apply chocks & lower rear legs if needed

6, Remove emergency brake cable or secondary coupling

Pull vehicle forward and reverse down side of trailer

Tell examiner that you would remove trailer plate if it is a shared trailer & not parked on the road

Recoupling  1 to 7

Check the trailer as if it is a unknown trailer using the trailer pre tow check list

Inc measuring the height of trailer hitch & tow ball to ensure it is set higher than the tow ball.

Once check is complete:-

Pull vehicle forward and reverse back to trailer ensuring you don't touch the trailer

If not already done check hitch & towball heights for clearance then reverse under the hitch

You can get out checking position as many times as you need as long as you are making progress

Check that you are in line with the trailer, tow vehicle handbrake securely on in neutral turn engine off KEY OUT

1, Connect the emergency brake cable or secondary coupling

If lowered raise rear legs & remove chocks

If not 100% aligned release the hand brake & manoeuvre the trailer by hand, reapply brake

2, Wind the jockey wheel so the coupling lowers over the ball lifting handle if needed locking the coupling in place, check visual indicators are showing

3, Wind the jockey wheel in the opposite direction to raise the back of the vehicle slightly to feel the cars weight to test the security of the coupling

4, Standard Jockey wheel

Wind the jockey wheel to the fully raised position and stow in the travelling position, use the locking pin if fitted

4, NEW STYLE JOCKEY WHEEL

Wind the jockey wheel to the fully raised position ensuring it is tight.

5, Connect the electrics

6, If not already done, raise the rear legs & fully release the trailer hand brake/remove chocks

7, Turn on vehicle lights and check all the lights are working and tell the examiner that you would replace the number plate if needed and ask him to check the brake lights are working.

Revision TWO 27/05/2018